Moore FSM Diagram

States
F0 = 0000
F1 = 0001
F2 = 0010
F3 = 0011
G0,2 = 0101
G1,3 = 0110
G2,0 = 1001
G3,1 = 1010
G0,3 = 1101
G3,0 = 1110
State Transition Table
Current State					Input		Next State					Output
Q3	Q2	Q1	Q0		B	A	Q3+	Q2+	Q1+	Q0+		Q1	Q0
0	0	0	0		0	0	0	0	0	0		0	0
					0	1	0	0	0	1		0	0
					1	0	0	1	0	1		0	0
					1	1	1	1	0	1		0	0

0	0	0	1		0	0	0	0	0	0		0	1
					0	1	0	0	0	1		0	1
					1	0	0	0	1	0		0	1
					1	1	0	1	1	0		0	1

0	0	1	0		0	0	1	0	0	1		1	0
					0	1	0	0	0	1		1	0
					1	0	0	0	1	0		1	0
					1	1	0	0	1	1		1	0

0	0	1	1		0	0	1	1	1	0		1	1
					0	1	1	0	1	0		1	1
					1	0	0	0	1	0		1	1
					1	1	0	0	1	1		1	1

0	1	0	1		X	X	0	0	1	0		0	1

0	1	1	0		X	X	0	0	1	1		1	0

1	0	0	1		X	X	0	0	0	0		0	1

1	0	1	0		X	X	0	0	0	1		1	0

1	1	0	1		X	X	0	1	1	0		0	1

1	1	1	0		X	X	1	0	0	1		1	0

Espresso Simplification
Input / #Elevator / .i 6 / .o 4 / Q In Q+ / 3210 BA 3210 / 0000 00 0000 / 0000 01 0001 / 0000 10 0101 / 0000 11 1101 / 0001 00 0000 / 0001 01 0001 / 0001 10 0010 / 0001 11 0110 / 0010 00 1001 / 0010 01 0001 / 0010 10 0010 / 0010 11 0011 / 0011 00 1110 / 0011 01 1010 / 0011 10 0010 / 0011 11 0011 / 0101 -- 0010 / 0110 -- 0011 / 1001 -- 0000 / 1010 -- 0001 / 1101 -- 0110 / 1110 -- 1001	Output / #Elevator / .i 6 / .o 4 / .p 16 / Q In D / 3210 BA 3210 / 0011 00 0100 / 000- 11 0100 / 0000 11 1000 / 0010 00 1001 * / 1101 -- 0100 / 000- 01 0001 / 1110 -- 1000 / 001- 11 0001 / 0011 0- 1010 * / 0000 1- 0101 * / 00-1 1- 0010 / -101 -- 0010 / 0-10 1- 0010 / 1-10 -- 0001 / 0110 -- 0011 * / --10 -1 0001 / .e
	Boolean Equations / D3 = Q3·Q2·Q1·Q0·B·A + Q3·Q2·Q1·Q0·B·A + Q3·Q2·Q1·Q0 + Q3·Q2·Q1·Q0·B / D2 = Q3·Q2·Q1·Q0·B·A + Q3·Q2·Q1·B·A + Q3·Q2·Q1·Q0 + Q3·Q2·Q1·Q0·B / D1 = Q3·Q2·Q1·Q0·B + Q3·Q2·Q0·B + Q2·Q1·Q0 + Q3·Q1·Q0·B + Q3·Q2·Q1·Q0 / D0 = Q3·Q2·Q1·Q0·B·A + Q3·Q2·Q1·B·A + Q3·Q2·Q1·B·A + Q3·Q2·Q1·Q0·B + Q3·Q1·Q0 + Q3·Q2·Q1·Q0 + Q1·Q0·A
	16 NOR Gates / 3 – 3 input NOR gates / 5 – 4 input NOR gates / 5 – 5 input NOR gates / 3 – 6 input NOR gates	4 OR Gates / 2 – 4 input OR gates / 1 – 5 input OR gate / 1 – 7 input OR gate
	32 Inverters
	4 D-Flip-Flops
	2 D-Latches
	1 – 2-Select Bits Priority Encoder
	1 – 2-Select Bits Decoder

Logisim Digital Circuit

Python MyHDL Code
from myhdl import always, always_comb, always_seq, Signal, ResetSignal, toVerilog, toVHDL, delay, traceSignals, Simulation, now, intbv, concat

#Implementation

def elevator(clk, reset, en, F, D, Q, A, B, A_latch, B_latch, LED):

   @always_comb
   def encoder():
      if bool(F) and en:
        A.next = bool(F[3] or (F[1] and not F[2]))
        B.next = bool(F[2] or F[3])

   @always_comb
   def latch():
      if reset:
        A_latch.next = bool(False)
        B_latch.next = bool(False)
      elif bool(F) and en:
        A_latch.next = A
        B_latch.next = B

   @always_comb
   def logic():
      D.next = concat( bool((not Q[3] and not Q[2] and not Q[1] and not Q[0] and B_latch and A_latch) or (not Q[3] and not Q[2] and Q[1] and not Q[0] and not B_latch and not A_latch) or (Q[3] and Q[2] and Q[1] and not Q[0]) or (not Q[3] and not Q[2] and Q[1] and Q[0] and not B_latch)),
        bool((not Q[3] and not Q[2] and Q[1] and Q[0] and not B_latch and not A_latch) or (not Q[3] and not Q[2] and not Q[1] and B_latch and A_latch) or (Q[3] and Q[2] and not Q[1] and Q[0]) or (not Q[3] and not Q[2] and not Q[1] and not Q[0] and B_latch)),
        bool((not Q[3] and not Q[2] and Q[1] and Q[0] and not B_latch) or (not Q[3] and not Q[2] and Q[0] and B_latch) or (Q[2] and not Q[1] and Q[0]) or (not Q[3] and Q[1] and not Q[0] and B_latch) or (not Q[3] and Q[2] and Q[1] and not Q[0])),
        bool((not Q[3] and not Q[2] and Q[1] and not Q[0] and not B_latch and not A_latch) or (not Q[3] and not Q[2] and not Q[1] and not B_latch and A_latch) or (not Q[3] and not Q[2] and Q[1] and B_latch and A_latch) or (not Q[3] and not Q[2] and not Q[1] and not Q[0] and B_latch) or (Q[3] and Q[1] and not Q[0]) or (not Q[3] and Q[2] and Q[1] and not Q[0]) or (Q[1] and not Q[0] and A_latch)) )

   @always_seq(clk.posedge, reset)
   def dff():
      if en:
        Q.next = D

   @always_comb
   def decoder():
      LED.next = concat( bool(Q[1] and Q[0]),
        bool(Q[1] and not Q[0]),
        bool(not Q[1] and Q[0]),
        bool(not Q[1] and not Q[0]) )

   return encoder, latch, logic, dff, decoder
Python MyHDL Verilog and VHDL Conversion Code
#Convert to Verilog

def convert():
   clk = Signal(bool(False))
   reset = ResetSignal(bool(False), bool(True), async=True)
   en = Signal(bool(True))
   F = Signal(intbv(0b0, 0b0, 0b10000))
   D = Signal(intbv(0b0, 0b0, 0b10000))
   Q = Signal(intbv(0b0, 0b0, 0b10000))
   A = Signal(bool(False))
   B = Signal(bool(False))
   A_latch = Signal(bool(False))
   B_latch = Signal(bool(False))
   LED = Signal(intbv(0b0, 0b0, 0b10000))
   toVerilog.timescale = "100ms/1ms"
   toVerilog(elevator, clk, reset, en, F, D, Q, A, B, A_latch, B_latch, LED)
   toVHDL(elevator, clk, reset, en, F, D, Q, A, B, A_latch, B_latch, LED)

convert()
Python MyHDL Simulation Code
#Simulate

def test_elevator():
   clk = Signal(bool(False))
   reset = ResetSignal(bool(False), bool(True), async=True)
   en = Signal(bool(True))
   F = Signal(intbv(0b0, 0b0, 0b10000))
   D = Signal(intbv(0b0, 0b0, 0b10000))
   Q = Signal(intbv(0b0, 0b0, 0b10000))
   A = Signal(bool(False))
   B = Signal(bool(False))
   A_latch = Signal(bool(False))
   B_latch = Signal(bool(False))
   LED = Signal(intbv(0b0, 0b0, 0b10000))
   elevator_inst = elevator(clk, reset, en, F, D, Q, A, B, A_latch, B_latch, LED)

   @always(delay(10))
   def clkgen():
      clk.next = not clk

   @always(delay(1))
   def stimulus():
      if now() == 45:
        F.next = Signal(intbv(0b0100))
      elif now() == 46:
        F.next = Signal(intbv(0b0000))
      elif now() == 60:
        F.next = Signal(intbv(0b0001))
      elif now() == 61:
        F.next = Signal(intbv(0b0000))
      elif now() == 150:
        F.next = Signal(intbv(0b0010))
      elif now() == 200:
        F.next = Signal(intbv(0b0011))
      elif now() == 250:
        F.next = Signal(intbv(0b0100))
      elif now() == 300:
        F.next = Signal(intbv(0b0101))
      elif now() == 350:
        F.next = Signal(intbv(0b0110))
      elif now() == 400:
        F.next = Signal(intbv(0b0111))
      elif now() == 450:
        F.next = Signal(intbv(0b1000))
      elif now() == 500:
        F.next = Signal(intbv(0b1001))
      elif now() == 550:
        F.next = Signal(intbv(0b1010))
      elif now() == 600:
        F.next = Signal(intbv(0b1011))
      elif now() == 650:
        F.next = Signal(intbv(0b1100))
        #reset.next = 0b1
      elif now() == 700:
        F.next = Signal(intbv(0b1101))
      elif now() == 750:
        F.next = Signal(intbv(0b1110))
      elif now() == 800:
        F.next = Signal(intbv(0b0001))
      elif now() == 850:
        F.next = Signal(intbv(0b1000))
        #reset.next = 0b0
      elif now() == 900:
        F.next = Signal(intbv(0b0010))
      elif now() == 950:
        F.next = Signal(intbv(0b1000))
        #en.next = 0b0
      elif now() == 1000:
        F.next = Signal(intbv(0b0001))
      elif now() == 1050:
        F.next = Signal(intbv(0b0100))
      elif now() == 1100:
        F.next = Signal(intbv(0b0001))
      elif now() == 1150:
        F.next = Signal(intbv(0b0100))
      elif now() == 1200:
        F.next = Signal(intbv(0b0000))
      elif now() == 1240:
        F.next = Signal(intbv(0b0000))
        #en.next = 0b1
      elif now() == 1360:
        F.next = Signal(intbv(0b0001))
      elif now() == 1370:
        F.next = Signal(intbv(0b1001))

   return elevator_inst, clkgen, stimulus#, reset_test, en_test

def simulate(timesteps):
   traceSignals.timescale = "100ms"
   tb = traceSignals(test_elevator)
   sim = Simulation(tb)
   sim.run(timesteps)

simulate(1500)

Verilog Code
// File: elevator.v
// Generated by MyHDL 0.8.1
// Date: Sun Jun 14 22:11:56 2015

`timescale 100ms/1ms

module elevator (
    clk,
    reset,
    en,
    F,
    D,
    Q,
    A,
    B,
    A_latch,
    B_latch,
    LED
);

input clk;
input reset;
input en;
input [3:0] F;
output [3:0] D;
wire [3:0] D;
output [3:0] Q;
reg [3:0] Q;
output A;
reg A;
output B;
reg B;
output A_latch;
reg A_latch;
output B_latch;
reg B_latch;
output [3:0] LED;
wire [3:0] LED;

always @(en, F) begin: ELEVATOR_ENCODER
    if (((F != 0) && en)) begin
        A = ((F[3] || (F[1] && (!F[2]))) != 0);
        B = ((F[2] || F[3]) != 0);
    end
end

always @(reset, A, B, en, F) begin: ELEVATOR_LATCH
    if (reset) begin
        A_latch = (1'b0 != 0);
        B_latch = (1'b0 != 0);
    end
    else if (((F != 0) && en)) begin
        A_latch = A;
        B_latch = B;
    end
end

assign D = {((((!Q[3]) && (!Q[2]) && (!Q[1]) && (!Q[0]) && B_latch && A_latch) || ((!Q[3]) && (!Q[2]) && Q[1] && (!Q[0]) && (!B_latch) && (!A_latch)) || (Q[3] && Q[2] && Q[1] && (!Q[0])) || ((!Q[3]) && (!Q[2]) && Q[1] && Q[0] && (!B_latch))) != 0), ((((!Q[3]) && (!Q[2]) && Q[1] && Q[0] && (!B_latch) && (!A_latch)) || ((!Q[3]) && (!Q[2]) && (!Q[1]) && B_latch && A_latch) || (Q[3] && Q[2] && (!Q[1]) && Q[0]) || ((!Q[3]) && (!Q[2]) && (!Q[1]) && (!Q[0]) && B_latch)) != 0), ((((!Q[3]) && (!Q[2]) && Q[1] && Q[0] && (!B_latch)) || ((!Q[3]) && (!Q[2]) && Q[0] && B_latch) || (Q[2] && (!Q[1]) && Q[0]) || ((!Q[3]) && Q[1] && (!Q[0]) && B_latch) || ((!Q[3]) && Q[2] && Q[1] && (!Q[0]))) != 0), ((((!Q[3]) && (!Q[2]) && Q[1] && (!Q[0]) && (!B_latch) && (!A_latch)) || ((!Q[3]) && (!Q[2]) && (!Q[1]) && (!B_latch) && A_latch) || ((!Q[3]) && (!Q[2]) && Q[1] && B_latch && A_latch) || ((!Q[3]) && (!Q[2]) && (!Q[1]) && (!Q[0]) && B_latch) || (Q[3] && Q[1] && (!Q[0])) || ((!Q[3]) && Q[2] && Q[1] && (!Q[0])) || (Q[1] && (!Q[0]) && A_latch)) != 0)};

always @(posedge clk, posedge reset) begin: ELEVATOR_DFF
    if (reset == 1) begin
        Q <= 0;
    end
    else begin
        if (en) begin
        Q <= D;
        end
    end
end

assign LED = {((Q[1] && Q[0]) != 0), ((Q[1] && (!Q[0])) != 0), (((!Q[1]) && Q[0]) != 0), (((!Q[1]) && (!Q[0])) != 0)};

endmodule

VHDL Code
-- File: elevator.vhd
-- Generated by MyHDL 0.8.1
-- Date: Sun Jun 14 22:11:56 2015

library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
use std.textio.all;

use work.pck_myhdl_081.all;

entity elevator is
    port (
        clk: in std_logic;
        reset: in std_logic;
        en: in std_logic;
        F: in unsigned(3 downto 0);
        D: inout unsigned(3 downto 0);
        Q: inout unsigned(3 downto 0);
        A: inout std_logic;
        B: inout std_logic;
        A_latch: inout std_logic;
        B_latch: inout std_logic;
        LED: out unsigned(3 downto 0)
    );
end entity elevator;

architecture MyHDL of elevator is

begin

ELEVATOR_ENCODER: process (en, F) is
begin
    if (bool(F) and bool(en)) then
        A <= stdl(bool(F(3)) or (bool(F(1)) and (not bool(F(2)))));
        B <= stdl(bool(F(2)) or bool(F(3)));
    end if;
end process ELEVATOR_ENCODER;

ELEVATOR_LATCH: process (reset, A, B, en, F) is
begin
    if bool(reset) then
        A_latch <= '0';
        B_latch <= '0';
    elsif (bool(F) and bool(en)) then
        A_latch <= A;
        B_latch <= B;
    end if;
end process ELEVATOR_LATCH;

D <= unsigned'((((not bool(Q(3))) and (not bool(Q(2))) and (not bool(Q(1))) and (not bool(Q(0))) and bool(B_latch) and bool(A_latch)) or ((not bool(Q(3))) and (not bool(Q(2))) and bool(Q(1)) and (not bool(Q(0))) and (not bool(B_latch)) and (not bool(A_latch))) or (bool(Q(3)) and bool(Q(2)) and bool(Q(1)) and (not bool(Q(0)))) or ((not bool(Q(3))) and (not bool(Q(2))) and bool(Q(1)) and bool(Q(0)) and (not bool(B_latch)))) & (((not bool(Q(3))) and (not bool(Q(2))) and bool(Q(1)) and bool(Q(0)) and (not bool(B_latch)) and (not bool(A_latch))) or ((not bool(Q(3))) and (not bool(Q(2))) and (not bool(Q(1))) and bool(B_latch) and bool(A_latch)) or (bool(Q(3)) and bool(Q(2)) and (not bool(Q(1))) and bool(Q(0))) or ((not bool(Q(3))) and (not bool(Q(2))) and (not bool(Q(1))) and (not bool(Q(0))) and bool(B_latch))) & (((not bool(Q(3))) and (not bool(Q(2))) and bool(Q(1)) and bool(Q(0)) and (not bool(B_latch))) or ((not bool(Q(3))) and (not bool(Q(2))) and bool(Q(0)) and bool(B_latch)) or (bool(Q(2)) and (not bool(Q(1))) and bool(Q(0))) or ((not bool(Q(3))) and bool(Q(1)) and (not bool(Q(0))) and bool(B_latch)) or ((not bool(Q(3))) and bool(Q(2)) and bool(Q(1)) and (not bool(Q(0))))) & (((not bool(Q(3))) and (not bool(Q(2))) and bool(Q(1)) and (not bool(Q(0))) and (not bool(B_latch)) and (not bool(A_latch))) or ((not bool(Q(3))) and (not bool(Q(2))) and (not bool(Q(1))) and (not bool(B_latch)) and bool(A_latch)) or ((not bool(Q(3))) and (not bool(Q(2))) and bool(Q(1)) and bool(B_latch) and bool(A_latch)) or ((not bool(Q(3))) and (not bool(Q(2))) and (not bool(Q(1))) and (not bool(Q(0))) and bool(B_latch)) or (bool(Q(3)) and bool(Q(1)) and (not bool(Q(0)))) or ((not bool(Q(3))) and bool(Q(2)) and bool(Q(1)) and (not bool(Q(0)))) or (bool(Q(1)) and (not bool(Q(0))) and bool(A_latch))));

ELEVATOR_DFF: process (clk, reset) is
begin
    if (reset = '1') then
        Q <= to_unsigned(0, 4);
    elsif rising_edge(clk) then
        if bool(en) then
        Q <= D;
        end if;
    end if;
end process ELEVATOR_DFF;

LED <= unsigned'((bool(Q(1)) and bool(Q(0))) & (bool(Q(1)) and (not bool(Q(0)))) & ((not bool(Q(1))) and bool(Q(0))) & ((not bool(Q(1))) and (not bool(Q(0)))));

end architecture MyHDL;

Waveform Viewer
Logic:

Reset and en:

The design can be improved by having the output going back and forth between extremes when multiple buttons are selected simultaneously, optimally by first going to the closest floor. This can be implemented with an additional FSM in place of the priority encoder.